## Slide 1
MAJOR PROJECT PANEL REVIEW · DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
ASTRA
Autonomous Safety-Trust Runtime Architecture
A layered runtime governance stack for learned controllers, and an experimental study of when its safety monitors can and cannot be trusted
PROJECT TEAM
Sushanth C.
USN: [NEEDS INPUT]
Tarun Gowda V
USN: [NEEDS INPUT]
T Tilak Reddy
USN: [NEEDS INPUT]
GUIDE
Dr. Chaitra R.
Department of Computer Science & Engineering
INSTITUTION
BMS College of Engineering, Bengaluru
Academic Year 2025-2026

## Slide 2
AT A GLANCE
Project overview
What ASTRA is
A nine-layer runtime safety architecture for a vehicle driven by a learned (reinforcement-learning) controller, together with an experimental testbed that injects controlled sensor faults and measures how each layer detects — or fails to detect — those faults.
What problem it addresses
Autonomous cyber-physical systems increasingly rely on learned controllers whose internal behaviour cannot be formally verified. Runtime safety monitors are placed around them to catch sensor faults and misbehaviour. Existing architectures assume these monitors work reliably. Our experiments show that this assumption fails in specific, measurable ways — including a monitor being silent during the very hazard it is designed to catch. ASTRA characterises these failures and proposes an architecture that assesses the trustworthiness of its own monitors at runtime.
Intended users
• Autonomous-vehicle and ADAS engineers designing runtime safety supervisors
• Safety analysts performing SOTIF (ISO 21448) coverage assessments
• Researchers in runtime verification and conformal prediction for control systems
PROJECT AT A GLANCE
6
experiment phases completed
~4,300
closed-loop simulation runs
9
architectural layers, verified
6
measurement defects self-caught
All results are from a synthetic driving plant. External real-world validation is not yet in scope for the current stage.

## Slide 3
THE REAL-WORLD PROBLEM
Problem statement
The problem, precisely stated
A learned controller in a vehicle depends on sensor input. Sensors fail — bias, drift, dropout, noise, stuck values. Around the learned controller a safety supervisor runs runtime monitors intended to detect these failures and switch to a safe fallback before harm occurs.
The safety of the whole system therefore depends on the monitors being reliable. Every published safety architecture we surveyed assumes this without measurement.
Why this matters
• Safety standards (ISO 26262 functional safety, ISO 21448 SOTIF) require coverage arguments for how faults are detected — those arguments rest on monitor reliability.
• A monitor that is silent during a hazard is worse than one that misses it: silence reads as evidence of health, so the safe fallback is never engaged.
• There is no standard method to check whether a runtime monitor can, in principle, make a reliable decision before it is deployed.
Why a technological solution is required
Analytical verification of learned controllers is not feasible at scale. The pragmatic response is runtime monitoring, but runtime monitoring is currently designed and deployed without a discipline for assessing whether the monitor itself is trustworthy under the operating conditions it will actually see.
WHO EXPERIENCES IT
• Vehicle manufacturers integrating learned components in perception, prediction and control
• ADAS Tier-1 suppliers whose safety cases include runtime monitors
• Certification bodies asked to sign off on learned-controller safety arguments
• Downstream: passengers and vulnerable road users, whose safety depends on those monitors actually working

## Slide 4
WHY WE SELECTED THIS PROBLEM
Motivation
Real-world relevance
Learned controllers are already deployed at scale in production ADAS. Public data on their failure modes is limited, and the safety cases behind them lean heavily on runtime supervisors. If those supervisors have systematic blind spots, the assurance argument does not hold.
Existing pain points
• The Simplex architecture (Sha, 2001) is the field-standard runtime-assurance pattern but predates learned controllers and assumes the decision logic works.
• Conformal prediction gives elegant statistical guarantees under exchangeability, but no established procedure checks whether that assumption holds in a live system.
• Fault-detection literature evaluates a monitor at one location under one metric — typically AUC — and does not measure whether operational firing follows.
What motivated this system
We wanted a testbed where a fault could be traced through every layer of a governance stack, one variable at a time, with the discipline that any monitoring claim must survive delivered-signal verification and a pre-registered evaluation criterion. The testbed then produced the finding: monitors have systematic blind spots that no calibration alone repairs.
WHY EXISTING APPROACHES ARE INSUFFICIENT
Simplex (2001)
prescribes fallback controller and switching logic; does not prescribe how the decision logic itself is judged reliable
Innovation-based FDI
detects at one stage; not routinely evaluated against a learned controller's downstream behaviour
Conformal prediction
provides coverage under exchangeability; live systems routinely violate exchangeability without warning
Digital-twin / model-based
monitors residuals; assumes model and system stay aligned, an assumption that itself needs checking
Redundant sensor fusion
voting outvotes a liar and discards the evidence; fault correction becomes fault concealment

## Slide 5
WHAT WE SET OUT TO DO
Objectives
Six objectives, each traceable to a specific experimental deliverable in the project record.
1
Design a layered runtime governance architecture
Build a nine-layer stack around a learned proposer (Core-A) with a one-way trust boundary to a safety domain (Core-B). Verify every layer is domain-mapped and every safety gate returns a verdict on every control tick.
2
Build a controlled fault-injection testbed
Six fault classes across three sensor channels, delivered-signal verification, pre-registered evaluation windows and thresholds. Testbed used to run 4,300 closed-loop simulation runs.
3
Characterise stage-wise fault observability
For each fault and each layer, measure a stage-wise discriminability score. Produce an observability profile that shows where evidence of the fault survives and where it does not.
4
Establish calibration and detection behaviour of a conformal safety monitor
Systematically calibrate the statistical gate under three schemes; measure per-run false-alarm and detection behaviour; report the mechanism when it fails.
5
Separate statistical discriminability from operational detectability
Show, with data, whether a stage where the fault is statistically distinguishable also permits an operational monitor to fire reliably.
6
Propose an architectural response — a self-trust layer
Design ASTRA 2.0, a monitoring architecture that assesses whether its own monitors can be trusted at runtime. Design published; implementation is future work.
Objectives 1-5 are complete or substantially complete; objective 6 is designed with a validation plan pending implementation.

## Slide 6
LITERATURE SURVEY
Existing systems and identified gap
Approach | Core idea | Strength | Limitation for our setting
Simplex (Sha 2001) | Complex controller + safety controller + switching logic | Formalised trust boundary; widely adopted | Assumes decision logic is reliable; no self-assessment
Analytical redundancy / FDI (Willsky 1976; Basseville & Nikiforov) | Detect faults from residuals or innovation statistics | Well-studied, model-based, provable under linear assumptions | Requires accurate model; typically single detector at one stage
Conformal prediction / ICP (Vovk, Shafer, Gammerman) | Non-parametric anomaly detection with coverage guarantees | Distribution-free under exchangeability | Exchangeability assumption routinely violated in live systems; no built-in check
Digital-twin monitoring (model-based diagnosis) | Compare live system output with a model of expected behaviour | Interpretable; supports what-if analysis | Twin fidelity itself must be maintained; drift is silent
Redundant sensor fusion (TMR, median voting) | Multiple sensors, majority vote rejects the outlier | Handles common single-channel faults | A well-crafted adversarial signal can hide inside the voting margin
Fault-injection studies (various) | Inject known faults, measure detector response | Empirical, comparable across systems | Typically evaluated at one stage; run-level statistics rarely reported
IDENTIFIED GAP
Existing runtime safety architectures assume their monitors work. There is no established, reproducible procedure that measures whether a runtime monitor can be trusted under the conditions it will actually see — before deployment or during it. ASTRA addresses this gap directly and demonstrates its necessity empirically.
References available in accompanying literature-review document; systematic review recorded as an in-progress deliverable.

## Slide 7
HOW ASTRA ADDRESSES THE GAP
Proposed system
The proposal in one sentence
A layered governance stack around a learned controller, plus a self-assessment mechanism that measures whether each monitor can currently be trusted, and routes decisions accordingly.
How it addresses the gap
• Separates two questions that existing systems collapse: is there evidence of a fault, and can a decision be made on that evidence?
• Instruments every layer — sensing, estimation, trust, proposer, twin, statistical gate, deterministic shield, fail-safe, arbitration — so fault evidence is measured, not assumed.
• Adds a monitorability metric that predicts whether a stage's decision statistic has the dynamic range and stability to support a reliable threshold, before deployment.
• Adds a phase-aware detection rule that distinguishes fault activity from post-fault recovery, so that a monitor's silence during the fault is not read as safety.
• Preserves the one-way trust boundary between the learned domain (Core-A) and the safety domain (Core-B) throughout.
What makes the approach useful
The self-assessment mechanism is what makes an operator able to say, at runtime, how much to trust the current output of a specific monitor. That is a capability no existing architecture in this space provides.
CONCEPTUAL VIEW
L1 sensing
L2 UKF estimator
L3 trust
L4 learned proposer (CORE-A)
L5 PINN twin
L6 conformal gate
L7 shield
L8 fail-safe
L9 arbitration
→
SELF-TRUST PLANE
measures each monitor's dynamic range, drift, and phase state
attaches a trust score to every verdict
The stack (L1-L9) is implemented and characterised. The self-trust plane is a design proposal justified by the current experimental findings.

## Slide 8
CONTROL AND DATA FLOW
System architecture
Sensor input → estimation → trust → learned proposal → twin prediction → statistical and deterministic gates → fail-safe → arbitration → actuation.
SENSORS IMU · GPS · LIDAR · CAN · fused frame
SHARED (perception & estimation)
L1
Sensor bus, staleness rule, per-channel health
L2a
UKF innovation (Mahalanobis distance)
L2b
Fast-state estimate ŷ, v̂, â
L3
Trust index (Mondrian conformal context)
CORE-A
L4
Learned proposer (PPO with PID-Lagrangian CMDP) Writes π_prop to Core-B; may not read Core-B artefacts.
CORE-B (safety gates, verdict on every tick)
L5
PINN twin — physics-based command prediction
L6
Statistical (conformal) gate — non-conformity score
L7
Deterministic shield + physical envelope
L8
Fail-safe FSM
L9 ARBITRATION → actuation (issues the safe command; records the audit-trail record)
OBSERVABILITY PLANE (offline; read-only taps into every layer above)
Fault-evidence profiler · stability analyzer (σ_between, n_eff, autocorrelation) · monitorability M(f,s) · fault-evidence ledger · redundancy-consistency monitor
The observability plane never writes to Core-A. It is a monitor for the monitors, and it is the substrate for the self-trust mechanism in ASTRA 2.0.
Diagram based on `src/astra/` module layout; 9/9 layers domain-mapped; 3/3 Core-B gates verdict on every one of 300 ticks in a live verification run.

## Slide 9
HOW A CONTROL TICK IS PROCESSED
Workflow and methodology
Every 50 ms (20 Hz fast rate), the following sequence executes for one control tick.
1
Sensor acquisition
IMU/GPS/LIDAR/CAN publish into a shared bus. Timestamps and per-channel health are recorded. Redundant sensing draws independent noise per channel from a disjoint seed.
2
L1 fusion & health check
Frame assembled; L1 evaluates staleness against a 50 ms budget and flags per-modality health.
3
L2 estimation (dual-rate UKF)
Predict + update on the fused frame. Records the innovation vector, its Mahalanobis distance, and the covariance-normalised residual.
4
L3 trust classification
Context classifier (Mondrian scheme) assigns the tick to a context class (URBAN_CLEAR, HIGHWAY_CLEAR, DEGRADED_SENSOR); trust index emitted.
5
L4 (Core-A) proposes π_prop
Learned PPO policy consumes the fast state and trust and emits a command proposal. This is the only write from Core-A into Core-B.
6
L5 twin prediction
PINN twin produces the command that modelled physics expects, conditioned on the L3 context class.
7
L6 statistical gate
Compute non-conformity score = ‖π_prop − π_twin‖ / √P̂_a. Compare against the calibrated conformal quantile → PASS / VETO.
8
L7 shield + L7b physical envelope
Deterministic bounds on speed, lateral acceleration, jerk. VETO if any bound is exceeded.
9
L8 fail-safe FSM
Selects between issued command, degraded command, or halt posture based on gate verdicts and posture history.
10
L9 arbitration → actuation
Emits the safe command to the actuator; writes the full audit-trail record (fast state, proposal, gate verdicts, posture, seed).
Fault injection, when active, is applied at step 1/2 (sensor level) or step 5-6 (via the per-channel redundant sensing path). The rest of the pipeline is invariant.

## Slide 10
CHOSEN FOR REPRODUCIBILITY AND CONTROL
Technology stack
Language & runtime
Python 3.12
why: single language across pipeline, training and analysis; reproducibility trumps performance at this stage
PowerShell / Bash
why: orchestration; the project is CPU-only Windows 11
Numerical & ML
NumPy 2.5.1
why: primary numeric library; version pinned
PyTorch 2.13.0
why: neural policy and PINN twin; CPU inference
Stable-Baselines3 2.9.0
why: PPO implementation for the L4 policy
Gymnasium
why: training environment; NEVER imported by src/astra runtime
Statistics
statistics.NormalDist + custom impl
why: Wilcoxon, Holm-Bonferroni, BCa bootstrap, Spearman — hand-implemented to avoid mutating the runtime lockfile with scipy
Test & CI
pytest
why: unit + integration; 82 passed / 2 failing guard tests (pre-existing)
import-linter (contracts)
why: enforces Core-A → Core-B one-way boundary as architectural invariant
Documentation & artefacts
python-pptx (isolated venv)
why: presentation generation without touching the measurement lockfile
Markdown
why: every experiment carries protocol, integrity checks, decision log
Version control
git
why: branch `3.0`, six commits recording E17/E18/R1/R2/R3/R3b/R3c
Lockfile discipline is deliberate: adding scipy/matplotlib to the measurement venv would put every prior latency and gate measurement in question.

## Slide 11
THE THREE THAT CARRY THE PAPER
Core algorithms and technical approach
L2 UKF innovation
What it does · Unscented Kalman filter on the fast state; emits the innovation vector and its Mahalanobis distance under the innovation covariance.
Why chosen · Standard, well-understood non-linear estimator; innovation is the natural residual for FDI at the estimation stage.
Inputs / outputs · Fused sensor frame → posterior mean/covariance and residual statistics.
Notes · The innovation is the substrate for the L3 trust index and, in this study, for the D_L2a stage-wise discriminability.
L4 PPO with PID-Lagrangian CMDP
What it does · Learns a lateral-control policy under three constraint costs (comfort, envelope, actuator).
Why chosen · PID-Lagrangian is the standard treatment for constrained MDPs; PPO is sample-efficient and well-supported.
Training · Offline, on the synthetic driving environment (kinematic bicycle). Multipliers held fixed within a batch, updated between batches.
Notes · This is Core-A. Its output is the untrusted proposal π_prop. It is NEVER trained on real vehicle data in the current work.
L6 Inductive Conformal Prediction
What it does · Non-parametric anomaly gate: computes non-conformity score s = ‖π_prop − π_twin‖ / √P̂_a and thresholds against a calibration corpus quantile.
Why chosen · Distribution-free guarantee of false-alarm rate under exchangeability; no parametric assumption on the residual distribution.
Inputs / outputs · Proposal and twin prediction → score → PASS / VETO verdict.
Notes · Whether exchangeability actually holds is the whole subject of Phase 5 (E18 series). It didn't with the legacy corpus; policy-conditional recalibration restored it.
PRIMARY EVALUATION METRICS
D_s(f) — stage discriminability
AUC( T_s | faulted , T_s | matched-clean ), folded to [0.5, 1.0]. 0.5 = chance separability, 1.0 = perfect. Ticks pooled within a run.
Run-level false-alarm rate
|{t : score_t > q}| / |E_r| computed per run; unit of analysis is the run, never the tick.
Per-run FAR band [ε/2, 2ε]
At ε=0.05, band = [2.5%, 10%]. A calibration is 'valid' only if the majority of held-out clean runs fall inside this band.
Phase-resolved detection
During-fault and post-fault alarm rates reported separately. Aggregate rates would have hidden the R3b/R3c finding.

## Slide 12
MODULES AND INTEGRATION
Implementation
Repository structure (implemented)
• src/astra/ — nine-layer runtime governance stack (production code, no training deps)
• training/ — offline training for L4 policy and L5 twin; calibration harvest for L6
• benchmarks/ — experiment drivers (E17, E18, R1, R2, R3, R3b, R3c) and analysis
• tests/ — unit + integration + guard tests, contract enforcement
• research/ — experiment history, audits, invalidation records, claim ledger
• experiments/phase5_od8_h7/ — pre-registrations, frozen thresholds, decision logs
• results/ and var/policy/, var/twin/, var/calibration/ — artefacts, checkpoints
Key implementation decisions
• Runtime and training are import-separated: nothing in src/astra imports Gymnasium/SB3.
• Every experiment is pre-registered before running; the criterion is frozen on disk.
• Delivered-signal integrity check is a workflow requirement, not a coding convention — results without it are marked invalid.
• Invalidated results are retained with a WITHDRAWN flag; nothing is silently deleted.
• Statistical library is hand-implemented in numpy + stdlib to avoid mutating the measurement lockfile.
MODULE INTERACTION (SIMPLIFIED)
training.closed_loop.drive_closed_loop( )
→ constructs the pipeline, drives it for N ticks, calls an observer per tick, returns aggregate results
benchmarks.e18r3b_detect (example)
1. Load frozen threshold (v3, hard-coded) 2. For each fault × seed, run one clean + one faulted arm 3. Record per-tick scores; integrity-check delivered signal 4. Compute per-run alarm rate vs run-level decision boundary
SCREENSHOTS OF THE APPLICATION UI
[NEEDS INPUT] — the project has no user-facing UI; command-line drivers and generated PowerPoint / Markdown reports are the primary interfaces. Suggest: insert screenshots of the terminal running an experiment, and of a generated figure such as fig1_stage_profile_P1.svg.
Runtime code path is 21,631 SLOC; test code is 29,343 SLOC (>1:1 test-to-code ratio).

## Slide 13
WHAT IS COMPLETE AND WHAT IS IN FLIGHT
Current project status
COMPLETED
Architecture and runtime
• All 9 layers implemented and domain-mapped
• All 3 Core-B gates verdict on every tick (verified live on 300 ticks)
• Core-A → Core-B one-way boundary enforced by contract tests
Training pipeline
• L4 policy trained (three checkpoints: synthetic, long, jerkscaled)
• L5 PINN twin trained on kinematic bicycle dynamics
• L6 calibration corpus harvested
Experimental campaigns
• E17 30-seed sweep: 90 profiles, 2,160 runs
• E17 position re-injection: 720 runs (invalidated original claim)
• E18 calibration series: 72,000 clean ticks + 1,260 faulted runs
• E18-R1 (run-local), R2 (matched-pooled), R3 (long window), R3b (detection), R3c (sustained fault): together +720 runs
• Zero execution failures across ~4,300 runs
CURRENTLY IN PROGRESS / NEXT
Systematic literature review
Cross-check that the self-trust / monitorability contribution is unclaimed. In progress; blocks the novelty claim.
Phase 2 — Monitorability re-analysis
Compute M(f,s) on the 28 existing cells. Zero new compute, hours of work; validates or removes the paper's proposed metric.
P3 recalibration (E18-R4)
Fix P3 threshold bias identified in R3; short compute.
E19 — H7 monitor placement
Unblocked on P1 after E18-R3 PASS; awaits Phase 2 result before design finalisation.
Self-trust layer implementation
Design complete (ASTRA 2.0 review). Implementation as production code is the next major engineering task.

## Slide 14
WHERE THE PROJECT IS GOING
Roadmap — current stage to final demo
01
Completed
5 experiment phases; 4,300 runs; audited findings; withdrawn claims documented; ASTRA 2.0 architecture proposed
DONE
02
Current stage
Literature review + Phase 2 monitorability re-analysis + P3 recalibration + E19 pre-registration
IN PROGRESS
03
Next steps
Implement self-trust layer + phase-aware detector; complete E19 monitor placement study; run E20 lying-sensor extension on the per-channel injection path
NEXT
04
Final implementation
Integrated ASTRA 2.0 with observability plane, monitorability output, and phase-resolved decision rule
PLANNED
05
Testing & validation
comma2k19 real-driving-data replay (open-loop); CARLA closed-loop only if time permits; baseline comparison against innovation-χ² monitor
PLANNED
06
Final demo
Live end-to-end: inject faults into a driven scenario, show phase-resolved detection, show the self-trust plane annotating each verdict
PLANNED
Dates are deliberately not specified. Progression is gated: a stage is not entered just because it exists in the plan. External datasets follow, not lead, the internal causal chain.

## Slide 15
MEASURED, NOT ASSUMED
Results and preliminary findings
All results below are on the synthetic plant with three learned policy checkpoints. Positive findings are supported by ≥ 30 seeds and pre-registered criteria. External-data validation is future work.
Finding | Evidence | Status
OD-8 miscalibration is a calibration-set provenance failure, not a threshold-value one | Global recalibration reproduces the original defect exactly (0.00 % FAR on P1/P3, 11.06 % on P2) | Established
P1 conformal monitor: stable per-run false-alarm rate at a 160-second window | 30/30 held-out clean runs in the [2.5 %, 10 %] band at n = 3,200 (E18-R3) | Established
Windowed calibration limit was precision, not dynamics | Per-run FAR variance scales with n; slope −0.739 (P1), −0.918 (P3) (E18-R3) | Established
4 of 6 faults reach 100 % detection at n = 3,200 | position_bias, position_drift, lateral_noise, imu_dropout at 100 % (E18-R3b) | Established (with qualifier below)
A persistent sensor failure is invisible to the monitor for as long as it persists | Sustained imu_dropout, 160 s, 30 seeds: alarm rate 0.2 % — BELOW clean baseline of ~5 % (E18-R3c). R3b's 100 % detection was the post-fault recovery transient. | Established
Statistical discriminability does not predict operational detection | 17 of 28 cells disagree between D_L6 ≥ 0.9 and detection ≥ 0.9. D_L1 vs detection: Spearman ρ = −0.480, p = 0.0088 (E18) | Established
Fault-induced alarm suppression is a real phenomenon, not an anecdote | 11 of 28 cells, all p < 0.05. imu_dropout on P1: 0.10 % alarm during fault vs 5.47 % clean baseline (E18); phase-resolved mechanism confirmed by R3c | Established
Redundancy can conceal a fault entirely | POSITION_Y was inert against the driven sensing path for 17 days (E17-Position); Control C established causally: estimator sees 0 with redundancy on, 3.18 with it off | Established
Six earlier claims were withdrawn during the campaign after measurement defects were self-caught. All are documented in the project claim ledger; the discipline of recording them is itself part of the contribution.

## Slide 16
HONESTLY STATED
Challenges and limitations
Technical challenges encountered
• Six measurement defects self-caught during the campaign, five before publication. Each withdrew a claim and each was recorded rather than hidden.
• Original position-fault result was 0.5-by-construction: the redundant sensing path was regenerating the position channel from ground truth. Corrected by re-injecting through a per-channel path.
• Original P1 'VALID' calibration was measured on a different tick window than detection. Withdrawn once matched-window analysis exposed it.
• R3b's 100 % detection of imu_dropout was traced to the post-fault recovery transient, not the fault itself. R3c (duration-matched control) settled this.
How the team addressed them
• Adopted pre-registration: criterion frozen on disk before each experiment ran.
• Adopted delivered-signal integrity as a workflow requirement, not a coding convention.
• Adopted the run as the statistical unit; tick-level rates are now supplementary only.
• Maintain a machine-readable claim ledger; nothing is silently deleted.
Known limitations of the current work
• Synthetic plant only. All findings are [M-syn]; external validation [M-ext] is 0 of 30. This is the largest single limitation and the reason external datasets are the next stage.
• Three policies is not a sample of policies; findings on P1 do not automatically generalise across policy space.
• P2 is INVALID for fixed-quantile calibration (non-stationary score). Retained in the record; not tuned around.
• Two faults (speed_bias, speed_stuck) remain undetectable by the current L6 gate at any tested severity; their non-conformity score is flat in every phase.
• No end-to-end user-facing application; the deliverable is an audited testbed, measurement discipline, findings, and an architecture proposal.
• Self-trust plane is a design; implementation and validation are future work.
• Novelty of the specific self-trust framing awaits systematic literature review.
The withdrawal record is treated as an asset of the project: a reviewer can inspect exactly what was tried, what failed, and why, rather than only the polished result.

## Slide 17
REALISTIC EXTENSIONS
Future scope
Near-term (weeks)
Complete literature review (blocks the novelty claim); compute monitorability metric on the 28 existing cells (zero new compute); recalibrate P3 (short compute); run E19 monitor-placement experiment on P1 with pre-registered baselines.
Medium-term (months)
Implement the self-trust plane as production code with an interface, not a benchmark script. Run E20 (lying-sensor / adversarial): one channel lies within the voting margin using the redundancy-consistency monitor as the detection substrate.
External validation
comma2k19: open-loop replay of real driving data with controlled fault injection layered on top. Requires an adapter and confirmed timestamp precision.
Naturalistic regime validation
highD: naturalistic traffic trajectories to test whether findings survive across operating regimes rather than one synthetic driving profile.
Closed-loop realism
CARLA: closed-loop simulation with better sensor models; useful demonstration but not a substitute for real data.
Standards and industry engagement
Position monitorability + self-trust as a SOTIF (ISO 21448) coverage contribution; engage automotive R&D partners for real sensor data via NDA. Explicitly out of scope: any autonomy claim beyond fault detection and monitor assurance.

## Slide 18
IN SUMMARY
Conclusion
IN SUMMARY
Conclusion
Problem
Autonomous systems with learned controllers rely on runtime monitors that existing architectures assume are reliable. That assumption is not measured.
Proposed solution
ASTRA: a nine-layer runtime governance stack (Simplex-derived) instrumented so fault evidence is measurable at every stage, plus an observability plane that assesses whether each monitor can be trusted.
Current achievement
Six audited experiment phases, ~4,300 runs, zero fabricated results, six withdrawn claims documented. A working per-run-stable monitor on one policy at a 160-second window, four of six faults detectable, and — the most significant single finding — measured evidence that the monitor is silent for the duration of a persistent sensor failure.
Expected final outcome
An implemented self-trust plane, monitorability validated as a predictor of operational detection, and an initial external-data replication on comma2k19. Publishable at an IEEE conference in the runtime-assurance / dependability track.
Overall significance
The contribution is a shift from 'is there a fault?' to 'can the monitor answering that question currently be trusted?' — a distinction our own experiments show is necessary, and one no existing runtime-assurance architecture makes.