## Slide 1
6
experiment
phases run
4,290
closed-loop
runs executed
6
measurement defects
found, 5 self-caught
RESEARCH STATUS BRIEFING
ASTRA
Fault Observability and Operational
Monitoring in a Layered Governance Stack
Where does sensor-fault evidence stop being usable — and can that be turned into a working monitor?
Sushanth C. · Tarun Gowda V · T Tilak Reddy Guide: Dr. Chaitra R. · BMS College of Engineering · 1 September 2026

## Slide 2
INTRODUCTION
The problem we are working on
A sensor fault does not stay a sensor fault.
It passes through estimation, fusion, trust scoring and a stack of safety monitors. Each stage transforms it. Somewhere along that path the evidence that anything is wrong can become too weak for a downstream monitor to act on.
Conventional fault detection answers a binary question — “fault or no fault?” It does not tell an engineer WHERE in their own architecture the evidence stopped being usable, which is exactly what decides where a monitor should sit.
ASTRA is a 9-layer runtime governance stack for a learned controller, instrumented so that fault evidence can be measured at every stage.
The primary question
When a sensor becomes faulty, where in the pipeline does the fault stop being distinguishable from healthy behaviour?
Secondary question
Can that information decide where monitoring should occur?
Future security question
Does a deliberately manipulated sensor behave differently from a naturally faulty one?
NOT TESTED
Nine layers: L1 sensing · L2 dual-rate UKF · L3 trust · L4 learned proposer (Core-A) · L5 PINN twin · L6 conformal gate · L7 shield · L8 fail-safe · L9 arbitration.

## Slide 3
METHODOLOGY
How we measure
Four commitments that make the numbers mean something
1
Stage-wise discriminability
D_s(f) = AUC(faulted, matched-clean), folded to [0.5, 1.0]. 0.5 is chance-level separation, never “50 % accuracy”. Reported per stage as a profile, not collapsed to one number.
2
Delivered-signal integrity
A result is rejected unless the faulted arm is shown to differ from the clean arm at the point each consumer reads it. This rule exists because three earlier results were 0.5 by construction.
3
Pre-registration
Stage, faults, thresholds, tests and falsification criteria are written and frozen before execution. Deviations are reported as deviations.
4
The run is the unit
Ticks inside a run are autocorrelated and are never treated as independent samples. Changing tick→run overturned two of our own verdicts.
Metric appropriateness is audited per fault type: dispersion faults use a rolling-standard-deviation statistic, dropout uses stream health, bias and drift use the raw channel.

## Slide 4
ARCHITECTURE
The measurement surface
Verified in a live run, not read from documentation: 9 / 9 layers domain-mapped, 3 / 3 Core-B gates return a verdict on every one of 300 ticks.
L1
sensing
L2a
innovation
L2b
estimate
L3
trust
L4
proposer
L5
twin
L6
conformal
L7
shield
L8
fail-safe
L9
arbitration
SHARED L1–L3
CORE-A
CORE-B 3 gates, every tick
Stage | Statistic measured | What it tells us
L1 | raw channel value / dispersion / stream health | sensor-level detectability
L2a | UKF innovation (Mahalanobis distance) | estimator-level observability
L2b / L3 | estimated lateral position; trust index | post-estimation state and trust
L6 | conformal non-conformity score | statistical gate evidence — and its threshold
L7 / L8 | veto flag; fail-safe posture | operational gate outcome
The one-way Core-A → Core-B trust boundary is enforced by architectural invariants: Core-A may write a proposal into Core-B and may not read any Core-B artefact.

## Slide 5
NOVELTY
What is actually new
No single ingredient is novel. The proposed contribution is the combination — and its status is tracked honestly, item by item.
1
Stage-wise fault discriminability across a governance pipeline
ESTABLISHED
2
Fault-specific observability profiles — four distinct behaviours measured
ESTABLISHED
3
A candidate absorption point A(f), reported only where well-posed
PARTIAL
4
Separating statistical discriminability from operational gate detection
ESTABLISHED
5
Diagnosing why a conformal monitor fails, at the level of its score process
ESTABLISHED
6
Using measured observability to choose monitor placement (H7 / E19)
BLOCKED
7
Natural vs adversarial sensor manipulation (E20)
NOT TESTED
Novelty remains a research hypothesis until confirmed against a final systematic literature review and completed experiments. No priority claim is made.

## Slide 6
COMPARATIVE ANALYSIS
How this differs from existing practice
Dimension | Conventional FDI / residual monitoring | Conformal & runtime verification | ASTRA's position
Question asked | Is a fault present now? | Is this observation conformal to calibration? | Where does the evidence stop being usable?
Output | binary flag per detector | prediction set or alarm | a per-stage evidence profile D_f
Placement of monitors | engineering convention or intuition | wherever the score is defined | proposed to follow measured observability
Treatment of the estimator | residuals treated as the signal | estimator usually outside scope | estimator treated as a transformation that can remove evidence
Failure reporting | missed detection / false alarm rates | coverage guarantee | adds: does the gate have the dynamic range to fire at all?
What we add | — | — | a measured separation of discriminability, calibration validity and operational stability
The distinction the project has actually demonstrated
Statistical discriminability, calibration validity, and operational stability are three different properties. This system has the first without the third — measured, not argued.

## Slide 7
PROGRESS
Implementation roadmap and where we stand
E17
Fault observability
COMPLETE
E17-P
Corrected position injection
COMPLETE
E18
OD-8 calibration
COMPLETE
E18-R1
Run-local calibration
COMPLETE
E18-R2
Matched-window calibration
COMPLETE
E18-R3
Longer evaluation windows
NEXT
E19
H7 monitor placement
BLOCKED
comma2k19
Real-world data validation
NOT STARTED
highD
Traffic-regime validation
NOT STARTED
E20
Adversarial / lying sensor
NOT STARTED
CARLA
Closed-loop validation
NOT STARTED
◀ we are here
Completed
5 of 11 stages. All internal validation. 4,290 closed-loop runs, 0 execution failures.
Blocking the rest
E19 needs an operational monitor. E18-R2 established that no policy currently has one. E18-R3 is the gate.
Stages are gated: a stage is not entered because it exists in the plan. External datasets come after the internal causal chain, not before.

## Slide 8
CURRENT STATUS
Experiment ledger
Experiment | Question | Scale | Verdict | Outcome
E17 | Stage-wise fault observability | 90 profiles · 2,160 runs | COMPLETE | Observability is heterogeneous; 1 of 6 faults well-posed
E17-Position | Does absorption survive correct injection? | 720 runs | WITHDRAWN | Absorbed in 0 of 12 cells — original result was artefact
E18 | Can OD-8 be validly calibrated? | 72,000 ticks · 1,260 runs | PARTIAL | D_s does not predict detection; window defect found
E18-R1 | Does run-local calibration recover P3? | 60 runs | REJECTED | P3 9/30; mechanism removed, estimator too noisy
E18-R2 | Does matched-window calibration work? | reused scores | PARTIAL | P1 13/30 — best of three schemes, still short
4,290
closed-loop runs
0
execution failures
6
measurement defects found
5
of those, self-caught
0 / 30
external validation [M-ext]
Every invalidated record is retained and flagged, never deleted — an audit that erases its contaminated rows cannot be checked.

## Slide 9
RESULTS
What we have established
ESTABLISHED
Fault observability is heterogeneous
Four valid faults, four distinct behaviours: absorbed, absorbed-then-recovered, non-monotonic, persistent. A single absorption metric is ill-posed for five of six.
SUPPORTED
One clean absorption result
speed_stuck on policy P1: D 0.9625 → 0.5629 at the estimator, well-posed on 30/30 seeds, SD 0.0077.
ESTABLISHED
A fault-injection channel was inert for 17 days
POSITION_Y was regenerated from ground truth by the redundancy path. Demonstrated causally: estimator sees 0 with redundancy on, 3.18 with it off.
ESTABLISHED
Discriminability does not predict detection
17 of 28 cells disagree. D_L1 vs operational detection: Spearman ρ = −0.480, p = 0.0088 — the association runs backwards.
SUPPORTED
Fault-induced alarm suppression
11 of 28 cells, all p < 0.05. imu_dropout on P1 makes the monitor 55× LESS likely to alarm than clean operation — not better detection.
ESTABLISHED
Two faults are undetectable at any severity
speed_stuck and imu_dropout, correctly calibrated, on both valid policies. A property of the score, not of the threshold.
All results are [M-syn] — synthetic plant, three policies, one severity per fault where parameterisable. Thirty seeds buys reproducibility, not external validity.

## Slide 10
THE CENTRAL TECHNICAL FINDING
Why the monitor cannot be calibrated
The threshold is in the right place. The score has no room around it.
0.0097
score standard deviation (P1)
29 %
of ticks within ±0.01 of the threshold
0.005
threshold precision required
0.013–0.028
actual run-to-run baseline drift
Baseline shift | P1 false-alarm rate
−0.010 | 0.20 %
0 (calibrated) | 4.98 %
+0.010 | 29.17 %
+0.020 | 69.57 %
The problem in one sentence
The threshold must be placed to a precision of about 0.005 score units, while the score's own baseline wanders by 0.013–0.028 between runs.
The precision required is 3–6× finer than the system's own reproducibility. Signal-to-noise at the decision boundary is below 1.
Policy | Overdispersion vs binomial | Effective ticks (of 200) | Alarm autocorrelation | Mechanism
P1 | 4.2× | 11 | +0.359 | alarms cluster within a run
P3 | 9.2× | 2 | ≈ 0 | baseline varies between runs
An ideal monitor with independent ticks would place 29.2 of 30 runs in band. Three calibration schemes were tried; the best result for any policy was 13/30. The limit is the score process.

## Slide 11
CLAIMS DISCIPLINE
What we refuse to claim
Six measurement defects have been found in this project's own code — five by self-audit, before publication. Each one withdrew a claim.
WITHDRAWN
General L2a fault absorption
position faults never reached the estimator
WITHDRAWN
Position-fault absorption
0 of 12 cells after correct injection
WITHDRAWN
“Information is destroyed at L2a”
a downstream statistic recovers part of it
WITHDRAWN
L6 detection-without-response gap
the gate returns PASS on every tick
WITHDRAWN
H-regime operating-regime covariate
Simpson's paradox: pooled −0.341, within-policy +0.836
WITHDRAWN
OD-8 provides operational monitoring
no policy is calibrated on the evaluation window
Terminology we enforce
D = 0.5 is chance-level separation, never “50 % accuracy”.
High D never implies a gate fired.
Alarm suppression is not better detection.
Why this is a strength
Every withdrawal came from auditing a result that looked too clean. The workflow now requires delivered-signal verification before any sweep is believed.
Full status of every claim, with permitted wording, is maintained in CLAIM_LEDGER.md and updated after each experiment.

## Slide 12
FURTHER STAGES
Where this goes next
The immediate question is narrow, cheap, and decisive.
E18-R3
Longer evaluation windows
At 11 effective ticks per 200, matching an independent monitor implies ~3,600 ticks. A pure compute change. Separates “not enough samples” from “wrong monitor”.
NEXT
E19 / H7
Monitor placement
Does the observability profile predict where a monitor works best? The prediction stays derived from D_s and is pre-registered — even though E18 suggests it will fail.
BLOCKED
E20
Adversarial / lying sensor
One channel lies while two stay honest, through the per-channel injection path already built. Not started; no detection claim is made.
NOT STARTED
External
comma2k19 → highD → CARLA
Real driving data, then traffic regimes, then closed loop. Gated behind a working internal measurement chain.
NOT STARTED
If E18-R3 fails, the contribution reframes around the demonstrated limitation — a conformal score can separate faulted from clean runs at high AUC and still be unable to support a stable operational monitor. That is a real result.