## Slide 1
RESEARCH & COLLABORATION BRIEFING
ASTRA
Fault Observability, Information Loss & Monitor Placement
in Autonomous Driving Systems
Current Evidence • Research Roadmap • Dataset Validation • Industry Value • Publication Potential
Sushanth C. · Tarun Gowda V · T Tilak Reddy | Guide: Dr. Chaitra R. | BMS College of Engineering | 1 September 2026

## Slide 2
WHERE THE PROJECT STANDS
Executive summary
What exists today
An audited experimental framework
90 profiles · 2,160 closed-loop runs · 0 failures
Pre-registered before execution
Three measurement defects found and corrected — two by self-audit
The initial finding
Fault evidence weakens stage-by-stage,
and differently for different faults
One stable, well-posed result at n=30
Three other faults behave in three other ways
What is not yet known
Whether it generalises
No real-world data yet · no closed loop yet
Monitor-placement consequence untested
Adversarial extension not started
The ask
ASTRA has a technically audited foundation and a scientifically interesting initial finding. The remaining work is not feature development — it is a gated validation programme that determines whether the finding generalises to real data, adversarial conditions and closed-loop driving.
Every claim in this deck is badged ESTABLISHED / PARTIALLY VALIDATED / PLANNED / HYPOTHESIS and is traceable to the project's own audit documents.

## Slide 3
WHY THIS QUESTION IS NOT ALREADY ANSWERED
The problem
A sensor fault does not stay a sensor fault.
It passes through estimation, fusion, trust scoring and a stack of safety monitors. Each stage transforms it. Somewhere along that path the evidence that anything is wrong can become too weak for a downstream monitor to act on.
Conventional fault detection asks a binary question:
“fault or no fault?”
It does not tell an engineer WHERE in their own architecture the evidence stopped being usable — which is exactly what determines where a monitor should sit.
THE BLIND-SPOT PROBLEM
Sensor fault occurs
L1 sensing
evidence strong
L2 estimation
evidence weakens
L6/L7 gates
evidence insufficient
The monitor sits after the point where the evidence became insufficient — so it cannot act, however well it is implemented.
Illustrative schematic of the problem class. Measured per-fault profiles appear on the results slides.

## Slide 4
POSITIONING
What ASTRA actually does
A framework for quantifying how sensor-fault evidence changes across an autonomous-driving estimation and safety pipeline — identifying where discriminative evidence becomes insufficient for downstream detection, and investigating how that guides monitor placement.
The primary question
When a sensor becomes faulty, where in the pipeline does the fault stop being distinguishable from healthy behaviour?
Secondary question
Can that information decide where monitoring should occur?
Future security question
Does a deliberately manipulated sensor behave differently from a naturally faulty one? — not yet answered
ASTRA is NOT positioned as
✕ a sensor fault detector
✕ a Kalman-filtering contribution
✕ a CARLA testing exercise
✕ a multi-dataset benchmark
It measures how evidence about a fault survives
transformation — not whether a fault is present.

## Slide 5
NINE LAYERS, TWO ISOLATED CORES
The ASTRA pipeline
Measurement points used by the experiment are marked. Core-A proposes; Core-B may veto. The trust boundary is one-way.
L1
sensing
L2a
innovation
L2b
estimate
L3
trust
L4
policy CORE-A
L5
twin
L6
conformal
L7
shield
L8
fail-safe
L9
arbitration
SHARED · L1–L3
CORE-A
CORE-B · 3 gates verdict on every tick
ESTABLISHED
9 / 9 layers domain-mapped · 3 / 3 Core-B gates produce a verdict on every one of 300 ticks — verified in a live run, not from documentation.
Stage | Statistic measured | Role in the experiment
L1 | raw channel value / dispersion / stream health | sensor-level detectability
L2a | UKF innovation (Mahalanobis) | estimator-level observability
L2b | estimated lateral position | post-estimation state
L3 | trust index | normalised-innovation trust
L6 | conformal non-conformity score | statistical gate evidence
L7 / L8 | veto flag / fail-safe posture | operational gate outcome
Stage statistics are one defensible choice among several; a different statistic could move the measured values. Stated as a limitation throughout.

## Slide 6
AUDITED, 1 SEPTEMBER 2026
Current E17 status
E17 — NEEDS MINOR FIXES
Sweep audited: 4 of 6 faults passed injection integrity; 2 were invalid, have since been re-injected through the correct per-channel path, and re-run at n=30. Contaminated records are retained and flagged, not deleted.
Fault | Injection | 30-seed data | Current interpretation
speed_stuck | Valid | Valid | L2a — well-posed on 30/30 seeds (policy P1)
speed_bias | Valid | Valid | L2a modal 100 %, but 0/30 well-posed
lateral_noise | Valid | Valid | Persistent — never absorbed at any stage
imu_dropout | Valid | Valid | Non-monotonic — no well-posed A(f)
position_bias | Corrected | Re-run n=30 | NOT absorbed — D_L2a 0.675–0.797
position_drift | Corrected | Re-run n=30 | NOT absorbed — D_L2a 0.655–0.767
The two position faults, corrected and re-run
Re-injected via redundant.offset — the per-channel path. Fault
reached the estimator in 720/720 runs. Result: absorbed at L2a in
0 of 12 cells. The original D = 0.500 was entirely the artefact.
Why this strengthens rather than weakens the work
The defect was found by auditing our own headline result
because it looked too clean. The workflow now requires
delivered-signal verification before any result is accepted.

## Slide 7
READING THE METRIC CORRECTLY
What the current results mean
D_s = AUC(faulted, matched-clean), folded to [0.5, 1.0]. Unit of analysis is the seed, never the tick.
D = 0.5 does NOT mean “50 % accuracy”
0.5 is chance-level discriminability and the floor of a folded metric. It means the evaluated representation does not retain discriminative evidence — not that a detector is right half the time.
High D does NOT mean the gate fired
AUC is scale-free. It reports near-perfect separation for a shift far below a gate's decision threshold. Statistical separability and operational detection are different claims.
Fault-specific observability trajectories — four valid faults, four distinct behaviours
Fault | Behaviour | Absorption point A(f) | Evidence
speed_stuck | Absorbed at estimation | L2a — well-posed 30/30 (P1) | 0.9625 → 0.5629, SD 0.0077
speed_bias | Weakens, then statistic recovers | not well-posed — 0/30 seeds | modal L2a 100 % is misleading
imu_dropout | Non-monotonic | none — no unique A(f) | curve crosses and returns
lateral_noise | Persistent | none — never absorbed | stays separable throughout
position_bias / drift | Survives estimation (corrected) | none — not absorbed | D_L2a 0.655–0.797, n=30
PARTIALLY VALIDATED
Heterogeneity is the finding: a single absorption point is ill-posed for five of six faults. One fault-policy pair shows a clean, well-posed absorption.
One plant model · one severity per fault · three policies · simulation only. Reproducibility across seeds is not external validity.

## Slide 8
WHAT SURVIVED OUR OWN AUDIT
Validated vs invalidated
ESTABLISHED
▪ FaultChannel.POSITION_Y is inert against the driven sensing path under ADR-0033 — demonstrated causally (Control C: estimator sees 0 with redundancy on, 3.18 with it off), consistent across 9 policy/seed pairs.
▪ All nine layers are domain-mapped; all three Core-B gates verdict on every tick.
▪ The current L6 calibration prevents the gate from firing under the tested condition — classified as OD-8 / exchangeability violation, not a wiring defect.
▪ speed_stuck shows a stable, well-posed 30/30 absorption result at L2a under P1.
▪ Fault observability is heterogeneous across the valid faults.
▪ Invalid records are retained and flagged rather than deleted.
▪ The workflow now requires delivered-signal integrity verification before a sweep result is accepted.
WITHDRAWN
▪ “Position faults are absorbed at the estimator.” — the faults never reached the estimator. Re-injected correctly and re-run at n=30: absorbed in 0 of 12 cells (D_L2a 0.655–0.797). The original result was entirely artefact.
▪ “All 18 falsification checks negative.” — sound checks, contaminated data.
▪ The H-regime operating-regime claim — withdrawn as a Simpson's paradox: pooled ρ = −0.341, but within policy P2 ρ = +0.836.
▪ “Information is destroyed at L2a.” — a downstream statistic recovers part of it; the correct phrasing is that the evaluated representation does not retain discriminative evidence.
▪ “A detection-without-response gap at L6.” — the gate returns PASS on every tick; it never made a detection to ignore.
Three measurement defects were found in this project's own code, two of them by self-audit before publication. Each is documented with its cause and correction.

## Slide 9
STATED SO IT CAN FAIL
Current scientific hypothesis
Sensor-fault evidence degrades non-uniformly across pipeline stages, and the stage at which it becomes insufficient is a measurable, fault-specific property that can inform where monitors are placed.
Three concepts kept separate throughout — conflating them is the most common error in this area
Sensor-level detectability
▶
Estimator-level observability
▶
Downstream operational detectability
Can the fault be recognised from the raw corrupted measurement? | Does it remain distinguishable after state estimation? | Can a real gate, with its real threshold, act on it?
The distinction that currently matters most
A statistic can separate faulted from clean almost perfectly while the gate reading that statistic cannot fire, because the shift is far below its decision threshold.
This is why ASTRA reports statistical discriminability and operational detectability as separate quantities — and why the deck never presents one as the other.

## Slide 10
STATED AS A HYPOTHESIS, NOT A CLAIM
Novelty position
The novelty is not any single ingredient — each exists in the literature. The proposed contribution is the combination.
# | Proposed contribution | Status today
1 | Stage-wise fault discriminability across a governance pipeline | Measured on 4 valid faults
2 | Fault-specific observability trajectories | Measured — four distinct behaviours
3 | A candidate fault-absorption point A(f) | Ill-posed for 5 of 6 faults
4 | Separating statistical discriminability from operational gate detection | Measured — and consequential
5 | Using measured observability to investigate monitor placement | PLANNED — experiment H7
6 | Natural vs adversarial sensor manipulation | PLANNED — not started
7 | Simulation → real data → closed loop validation chain | PLANNED — gated
Novelty remains a research hypothesis until confirmed against a final systematic literature review and the completed experiments. No priority claim is made in this deck.

## Slide 11
THE NEXT SCIENTIFIC STEP
H7 — the monitor-placement experiment
PLANNED
The question
If a fault is distinguishable at one stage but not at a later stage, does monitoring at the earlier stage provide better operational detection?
This is where measured observability would become an engineering recommendation rather than an observation.
A binding constraint discovered first
Monitor calibration — not placement — is currently the
limiting factor. Under the tested condition the L6 gate
cannot fire: live non-conformity ≈ 3.39 against a
conformal quantile ≈ 5.40, a gap of ≈ 2.0.
H7 must therefore resolve, in order:
Can the monitor operate at all?
▶
Where does evidence remain sufficient?
▶
Does relocating it improve detection?
▶
Does it hold across faults & policies?
Because the first step is currently unresolved, H7 is gated behind the calibration question (OD-8). H7 has not succeeded and has not been run.

## Slide 12
EACH SOURCE ANSWERS ONE QUESTION
Dataset & validation strategy
Source | Purpose | Contributes | Weakness | Status
E17 (synthetic) | Controlled causal experimentation | fault injection, severity, seeds, stage-wise D, absorption, policy dependence | synthetic; not external validity | IN USE
comma2k19 | Real-world driving-data validation | does the E17 phenomenon transfer when driven by real vehicle data? | does not natively contain the required sensor faults | PLANNED
highD | Naturalistic traffic / regime validation | trajectories, speed distributions, density, following & lane-change behaviour | not a sensor-fault dataset | PLANNED
CARLA | Closed-loop validation & demonstration | faults, adversarial sensors, estimator behaviour, closed-loop consequences | must not be the sole source of evidence | PLANNED
Method note
Where a real-world dataset does not contain the required faults, controlled fault injection is applied over real measurements. This is stated as a method, not disguised as naturally occurring faults. Dataset availability and licensing are verified before a dataset is treated as a confirmed resource.

## Slide 13
AND WHAT NEITHER PROVES
comma2k19 and highD — what each is for
comma2k19 — real-world signal realism
Question: does the observability behaviour found in E17 survive when the pipeline is driven by real vehicle data?
Contributes raw GNSS, 9-axis IMU and CAN from real highway driving.
It does NOT natively contain the sensor faults being studied — controlled injection over real measurements is the method.
Status: conditional — verification of timestamp precision, storage, calibration and drive identity is outstanding.
highD — operating-regime realism
Question: do the results hold across realistic traffic regimes rather than one synthetic driving profile?
Contributes naturalistic trajectories, speed distributions, traffic density, following and lane-change behaviour.
It is NOT treated as a sensor-fault dataset. Its role is regime and generalisation validation only.
Status: planned, not started.
Additional dataset opportunities — only if scientifically justified
Categories under consideration: autonomous-driving datasets, localisation/sensor datasets, trajectory datasets, perception datasets, fault/diagnostic datasets, cybersecurity/attack datasets. More datasets do not automatically increase novelty — one is added only when it answers a specific unresolved question.
Current external-validation status: none. Every result in this deck is simulation-based. Thirty seeds buys reproducibility, not external validity — the two are routinely conflated and are not the same claim.

## Slide 14
FUTURE SECURITY DIRECTION
Adversarial / lying-sensor extension
PLANNED
Not started. ASTRA does not currently detect manipulated sensors and no such claim is made.
Honest sensor A
reports truth
Compromised sensor B
reports plausible falsehood
Honest redundant sensor C
reports truth
Sensor fusion / estimator
▼
ASTRA stage-wise observability
▼
Is the manipulation still visible?
The scientific question
Can ASTRA characterise whether deliberately plausible false measurements remain observable, or become hidden by sensor fusion?
A natural fault and a crafted one may occupy very different positions in the observability profile. That difference — if it exists — is the contribution.
Entry point already exists
redundant.offset(modality, tick)
A per-channel injection path added during the September audit. It makes one channel lie while others stay honest — which is precisely the adversarial configuration, and is the same mechanism needed to fix the position faults.

## Slide 15
STAGES ARE GATED, NOT SEQUENTIAL BY DEFAULT
Gated validation roadmap
1. E17 audit
▶
2. Fix position injection
▶
3. Correct L6 interpretation
▶
4. Confirm speed_stuck metric
5. Corrected E17 validation
▶
6. H7 monitor placement
▶
7. comma2k19 real data
▶
8. highD regime validation
9. Adversarial sensors
▶
10. CARLA closed loop
▶
11. Integrated evaluation
▶
12. Conference paper
13. Expanded journal paper
Gating rule
A stage is not entered because it exists in the roadmap. Each must answer a specific unresolved scientific question, and the preceding stage must have produced evidence that justifies it. CARLA is deliberately last and is not presented as a source of primary evidence.

## Slide 16
POTENTIAL VALUE — TO BE VALIDATED
Why would a company care?
1 Better monitor placement
Move from intuition-based or convention-based monitor siting to evidence-based guidance: monitor where fault evidence still exists.
fewer blind spots · better diagnostic coverage · better use of compute
2 Safety validation
Answer “which sensor faults become invisible after state estimation?” before deployment rather than after.
find monitor blind spots · identify failure modes · prioritise testing
3 Sensor-fusion robustness
As GNSS, IMU, odometry, camera, LiDAR and radar are fused, ask what happens to fault evidence after fusion.
framework for reasoning about fusion-induced evidence loss
4 Cybersecurity extension
If the adversarial work succeeds: which manipulations stay detectable after fusion, and which do not?
security testing · attack-surface analysis · redundancy evaluation
All four are POTENTIAL benefits contingent on the validation programme succeeding. No cybersecurity protection is promised, and no company benefit has yet been demonstrated on company data.

## Slide 17
WHAT THE OUTPUT COULD BECOME
Engineering decision support
TODAY — binary detection
Fault occurs
▶
Detector: “fault / no fault”
Limited information about where the fault became invisible.
POTENTIAL WITH ASTRA — stage-wise profile
L1 sensing
visible
L2 estimation
visible
L2a innovation
weak
L7 shield
insufficient
→ “the architecture has a monitoring blind spot here”
Possible future output format
fault → stage where evidence weakens → recommended monitor location → confidence
What we could offer a collaborating company — potential directions, not existing partnerships
▪ validation on company-specific sensor architectures
▪ safety-monitor evaluation and blind-spot analysis
▪ sensor-fusion robustness and fault-injection scenarios
▪ adversarial sensor testing (once validated)
▪ CARLA / digital-twin closed-loop validation
▪ benchmarking and joint publication or technical report

## Slide 18
QUALITATIVE, NOT PROBABILISTIC
Credibility assessment
Dimension | Current status | After the roadmap
Experimental integrity | Strong — independently audited | Strong
Controlled validation | Developing — E17, 4 valid faults | Strong — E17 expanded
Statistical confidence | Developing — n=30 seeds, CIs reported | Strong
Real-world validity | Low — none yet | Promising — comma2k19
Regime validation | Low — none yet | Promising — highD
Monitor-placement evidence | Low — H7 not run | Promising — H7
Adversarial validation | Low — not started | Developing — planned
Closed-loop validation | Low — not started | Promising — CARLA
Industry relevance | Developing — potential only | Promising after validation
Conference readiness | Developing | Potentially strong
Journal (Q2) readiness | Low | Potentially strong
Journal (Q1) readiness | Low | Depends on final evidence
Labels are qualitative by design: Low · Developing · Promising · Strong · Submission-ready. No acceptance probability is quoted, because none can be responsibly estimated.

## Slide 19
THREE TIERS, EACH WITH EXPLICIT PREREQUISITES
Publication pathway
IEEE Conference
▪ corrected E17
▪ reproducibility
▪ statistically defensible results
▪ clear novelty positioning
▪ H7 evidence
▪ meaningful external validation
▪ clearly stated limitations
Strong conference potential IF the remaining validation confirms the central hypothesis.
Q2 Journal
▪ everything above, plus
▪ real-world validation
▪ strong ablations
▪ full statistical analysis
▪ reproducibility package
▪ clear engineering implications
A rigorous empirical paper could form a strong Q2 submission.
Q1 Journal
▪ novel phenomenon
▪ statistical reproducibility
▪ independent real-world validation
▪ mechanistic explanation
▪ monitor-placement consequence
▪ adversarial extension
▪ closed-loop CARLA validation
▪ strong baselines + ablations
Q1 requires substantially stronger evidence than exists today.
No acceptance probability can be guaranteed. The objective is to make the scientific contribution strong enough for a credible submission.

## Slide 20
WHAT WE SAY, AND WHAT WE REFUSE TO SAY
Claims discipline
ESTABLISHED
What we can officially claim today
✓ POSITION_Y is inert under ADR-0033 — causally demonstrated (Control C)
✓ 9/9 layers domain-mapped; 3/3 Core-B gates verdict every tick
✓ Current L6 calibration prevents firing under the tested condition (OD-8)
✓ speed_stuck: stable well-posed 30/30 absorption at L2a under P1
✓ Fault observability is heterogeneous across the valid faults
✓ The H-regime claim was withdrawn (Simpson's paradox)
✓ Invalid records are retained and flagged, not deleted
✓ Delivered-signal integrity verification is now required before acceptance
✓ Corrected position faults are NOT absorbed at L2a — 0 of 12 cells, n=30
MUST NOT CLAIM
What we refuse to claim
✕ universal fault absorption
✕ that position faults are currently absorbed
✕ that all faults have validated absorption points
✕ that D = 0.5 means “50 % accuracy”
✕ that high D means an operational gate fired
✕ that ASTRA already detects hacked sensors
✕ that ASTRA is proven Q1-worthy
✕ guaranteed conference or journal acceptance
✕ that more datasets automatically create novelty

## Slide 21
WHY WE SHOULD CONTINUE
1. Controlled science
2. Fault observability
3. Estimator interaction
4. Monitor placement
5. Real-world validation
6. Traffic-regime validation
7. Adversarial sensors
8. Closed-loop safety
9. Industry validation
The current E17 result is not the final product. It is the controlled foundation for testing a broader hypothesis across increasingly realistic environments.
ASTRA already has a technically audited foundation and a scientifically interesting initial finding. The remaining work is not random feature development: it is a gated validation programme that can determine whether the finding generalises to real data, adversarial conditions and closed-loop autonomous driving — and whether it can become both an industry-relevant engineering capability and a strong academic contribution.
The goal is not to expand the project artificially. It is to determine whether the observed phenomenon is real, reproducible, generalisable and practically useful.